## Slide 1: Long Term Effect of Bioresorbable Scaffolds and Metallic Drug Eluting Stents on Human Coronary Hemodynamics. Results of the Absorb II Randomized Trial Physiology Substudy
Javier Escaned MD PhD, on behalf of the
Absorb II Physiology Substudy Team

## Slide 2
Javier Escaned MD PhD
I have the following disclosures to report in the field of this presentation:
Speaker at educational events and/or consultancies: Abbott, Philips Healthcare

## Slide 3: Background
The long-term effect of bioresorbable vascular scaffold (BRS) on epicardial coronary vessels and the subtended microcirculation, compared to implanted metallic stents, remains largely unknown.
This missing information is key in supporting the overall concept of vascular restoration therapy and, thereby informing further advancement in this technology.

## Slide 4
In this sub-study of the ABSORB II trial 1 we compared long-term functional aspects of coronary vessels and the microcirculation after BVS or EES implantation.
Patients undergoing scheduled 3 year follow-up follow-up angiography at 3 ABSORB II centres in The Netherlands underwent physiological interrogation of the treated vessel with intracoronary flow velocity and pressure.
Obtained tracings were analyzed at a core laboratory, blinded to randomization, clinical and angiographic data. A per-vessel analysis was performed.
Study design
1) Serruys PW et al. Lancet 2016;388:2479-2491.

## Slide 5
A glossary of physiological indices used
Index | Type of information
Epicardial conductance1 | Effective blood transportation through the epicardial vessel
Microcirculatory conductance2 | Degree of microvascular structural remodelling
Zero flow pressure3 | Extravascular compression of capillaries
Forward waves distal to PCI site4 | Viscoelasticity of PCI-treated segment
Backward expansion wave5 | Capillary density downstream treated vessel
Van de Hoeven N et al. EuroIntervention. 2019:14:e1593-e1600.
Escaned J et al. Circulation 2009: 20(16):1561-8
Teunissen PF et al. Circ Cardiovasc Interv. 2015;8:e001786.
4) Davies JE et al Am J Physiol Heart Circ Physiol. 2006;290:H878-85.
5) Broyd C et al. Eur Heart J. 2018;39:1807-1814

## Slide 6
EKG, hyperemic pressure (Pa and Pd) and flow velocity were used to generate pressure-velocity loops. From these, diastolic conductance of the epicardial vessel (Cepi) and the microcirculation (Cmicro) were calculated separately. Zero flow pressure (Pzf, red circle) was also calculated
Flow velocity (cm/s)
Pressure (Pa, Pd) (mm Hg)
Pressure (Pa, Pd)
Flow velocity
Physiological interrogation / Coronary conductance
Van de Hoeven N et al. EuroIntervention. 2019:14:e1593-e1600.
IHDVPS Pd
IHDVPS Pa
Cmicro = IHDVPSPd
Cepi =
IHDVPSPd x IHDVPSPa
IHDVPSPd - IHDVPSPa
IHDVPS: Instantaneous hyperemic diastolic velocity pressure slope

## Slide 7: Physiological interrogation / Wave intensity
EKG, resting pressure (Pa and Pd) and flow velocity were used to perform wave intensity analysis. From this, forward and backward waves in the coronary circulation were calculated separately.
Forward wave
Davies J et al Circulation. 2006;113(14):1768-78.

## Slide 8: Study population
31 patients /32 vessels initially included
3 patients excluded due to suboptimal physiological tracings.
Study population: 28 patients / 29 vessels
No significant diferences in age, gender, cardiovascular risk factors, renal function or treated vessel between EES- and BRS-treated patients.

## Slide 9: Pre-procedural and post-PCI data
 | BRS (n=13) | EES (n=16) | P value
Diameter stenosis (%) | 61 ± 9 | 62 ± 12 | 0.850
Lesion length (mm) | 13 ± 5 | 11 ± 3 | 0.259
Reference vessel (mm) | 2.7 ± 0.4 | 2.5 ± 0.3 | 0.310
Device diameter (mm) | 3.1 ± 0.2 | 3.0 ± 0.2 | 0.139
In-stent diameter stenosis after PCI (%) | 16 ± 6 | 8 ± 6 | 0.004

## Slide 10: 3-year angiographic and FFR results
 | BRS (n=13) | EES (n=16) | P value
Reference vessel (mm) | 2.74 ± 0.40 | 2.58 ± 0.31 | 0.333
In-stent MLD (mm) | 2.13 ± 0.46 | 2.26 ± 0.35 | 0.478
In-stent diameter stenosis (%) | 22 ± 9 | 13 ± 7 | 0.01
Late loss (mm) | 0.24 ± 0.25 | 0.18 ± 0.28 | 0.601
FFR | 0.91 ± 0.04 | 0.91 ± 0.07 | 0.902

## Slide 11: Physiological findings in epicardial vessels (3Y FU)
Epicardial conductance
Fwd compression wave
Fwd expansion wave

## Slide 12
BEW
BEW
Reflected waves as a result of compliance mismatch caused by permanent stent, attenuated forward wave transmission.
Better forward wave transmission in segment with preserved viscoelasticity after BRS resorption.
Rationale for improved wave transmission in BRS

## Slide 13: Physiological findings in the microcirculation (3Y FU)
Microcirculatory conductance
Zero flow pressure
Backward expansion wave

## Slide 14: Conclusions
In the long-term, implantation of BRS results in better epicardial vessel function than EES, with
a) better epicardial conductance
b) preserved viscoelastic properties and transmission of flow waves
In the long-term, BRS use was not associated to better microvascular function than EES.
These findings support the existence of favourable long-term differences in vascular mechanics of BRS-treated vessels, as compared with those treated with metallic stents.

## Slide 15: ABSORB II Physiology Substudy Team
Principal Investigator: Patrick W. Serruys – Rotterdam, NL
Co-Principal Investigator: Bernard Chevalier – Massy, FR
Physiology substudy PIs: Javier Escaned – Madrid, ES
                Yoshinobu Onuma - Rotterdam, NL
                Patrick W. Serruys – Rotterdam, NL
                Jan Piek – Amsterdam, NL
Physiology substudy site PIs: Rene van der Schaaf – Amsterdam, NL
                Robert Jan van Geuns – Rotterdam, NL
                Jan Piek – Amsterdam, NL
Physiology substudy team members: A Quiros, T Asano, HJ Lee, C Broyd, Y Katagiri, T van der Hoef, M Echavarría-Pinto, N Gonzalo, N van der Hoeven, J Davies
Imaging Core Laboratory: Cardialysis – Rotterdam, NL
Sponsor: Abbott Vascular – Santa Clara, USA