## Slide 1: 1-Year Clinical and Imaging Outcomes of a Novel Ultra High Molecular Weight PLLA Sirolimus-Eluting Coronary BRS: A Prospective Multicenter International Investigation (The FORTITUDE® Study)
Boris Vesga, Hector Hernandez, Miguel Moncada, Alaide Chieffo, Azeem Latib, Eugenio Stabile, Giovanni Esposito, Antonio Dager, Jaime Fonseca, Camilo Arana, Juan A. Delgado, Emanuele Meliga, Tiziana C. Aranzulla, German Gomez, Giuseppe Tarantini, Alessio La Manna, Corrado Tamburino, Juan F. Granada
Antonio Colombo, MD
Ospedale San Raffaele, Milan, Italy

## Slide 2: Disclosure Statement of Financial Interest
I, (insert name here), DO NOT have a financial interest/arrangement or affiliation with one or more organizations that could be perceived as a real or apparent conflict of interest in the context of the subject of this presentation

## Slide 3: FORTITUDE Study Design
Patients Eligible for PCI of Single De Novo Native Coronary Artery Lesion
Baseline Angiography: < 14 mm Length, Severe Calcification Excluded
Baseline IVUS: Vessel Size 2.5 – 3.7 mm, Severe Calcification Excluded (n=63)
Mandatory Pre-Dilatation (Target <40% DS)
Scaffold implantation (n=62): Based on IVUS Measurements
Optimal Angiographic Result (40/62= 65%)
Sub-Optimal Angiographic Result (22/62= 35%)
Post-Dilatation NC-Balloon
Post-Deployment OCT
9-Month Angio-OCT Follow Up (n=60)
2-Year Angio-OCT or CT-Angio F/U
Clinical Follow Up 3,4,5 Years
 1 Failure to Cross
 1-Non-Cardiac Death, 1-Lost in Follow Up

## Slide 4: FORTITUDE® Sirolimus Eluting BRS: Device Characteristics
Design Feature | Description
Polymer | Ultra High MW-Poly-L-Lactide (PLLA)
Diameters | 2.75, 3.0, 3.5, and 3.75 mm
Lengths | 13 and 18 mm
Wall Thickness | 150 µm All Scaffold Sizes
Surface Coverage Area | 20 to 24%*
Drug Coating | 1:1 Poly D L-lactide:Sirolimus
Drug Content | 101 to 160 µg*
Drug Density | 96 µg/cm2
Inflation Pressures | Nominal: 6 to 8 ATM RBP: 15 to 16 ATM
Guide Catheter Size | 6 French Compatible
*Depending on scaffold size

## Slide 5: Enrollment Sites (Italy and Colombia) and Number of Patients per Site

## Slide 6
Nothing to disclose

## Slide 7: Baseline Clinical Characteristics
Baseline Characteristics | FORTITUDE® DES (n = 63) Mean ± SD or % (n)
Male | 77.8% (49)
Age (Years) | 63.7 ± 11.0
History of Smoking | 60.3% (38)
Medically Treated Diabetes Insulin Requiring Non-Insulin Requiring | 30.2% (19) 31.6% (6) 68.4% (19)
Medically Treated Hypertension | 81.0% (51)
History of Renal Disease | 9.5% (6)
Clinical Presentation | 
Stable Angina | 54.0% (34)
Acute Coronary Syndrome | 34.9% (22)
Silent Ischemia | 11.1% (7)
Previous MI | 38.1% (24)
History of PCI | 60.3% (38)
History of CABG | 4.8% (3)
LVEF | 55% ± 8.5%

## Slide 8: Angiographic Lesion Characteristics
Baseline Characteristics | FORTITUDE® DES (n = 63) Mean ± SD or % (n)
Target Artery LAD LCX RCA | 38.1% (24) 28.6% (18) 33.3% (21)
Lesion Location Proximal-Mid | 92% (58)
Reference Vessel Diameter (mm) | 2.9 ± 0.5 (63)
QCA Diameter Stenosis | 60.1% ± 10.1% (63)
QCA Length (mm) | 12.5 ± 3.0 (63)
ACC/AHA Lesion Class Type B1-B2 | 88.9% (56)
Any Bifurcation/Side Branch | 12.7% (8)
Calcification Moderate-Severe | 9.5% (6)
Pre-Procedure TIMI 3 Flow | 95.2% (60)

## Slide 9: Device Implantation: Procedural Endpoints
Index Procedure Characteristics (QCA) | FORTITUDE® DES (n = 63) Mean ± SD or % (n)
Pre-Procedure Diameter Stenosis | 60.1% ± 10.1% (63)
Pre-Dilatation Prior to Implant | 100% (63)
Single Post-Dilatation using NC Balloon | 34.9% (22)
Max. Scaffold Deployment Inflation Pressure (ATM) | 12.3 ± 2.8 (62)
Final In-Segment Diameter Stenosis | 14.1% ± 10.9% (63)
Failure to Cross Due to Severe Calcification/Tortuosity | 1.6% (1)
Distal Dissection Treated with DES1 | 4.8% (3)
Clinical Device Success2 | 98.4% (62)
Clinical Procedure Success3 | 96.8% (61)
1Non-flow limiting dissections identified distal and outside of scaffold; BRS-DES overlap not required
2Defined as successful delivery and deployment of the scaffold at the intended target lesion with final residual stenosis of <50% of the target lesion by QCA after the index procedure.
3Defined as clinical device success with any adjunctive device without the occurrence of major adverse clinical events related to ischemia up to day of discharge.

## Slide 10: 9-Month Angiographic Analysis
QCA Measurements Mean ± SD (n) | Baseline Procedure (n=63) | Post-BRS Implantation N=63 | 9-Month Follow-Up N=60 | p-Value
In-Segment Analysis |  |  |  | 
Interpolated RVD (mm) | 2.9 ± 0.5 | 2.9 ± 0.4 | 2.8 ± 0.5 | 0.0011
MLD (mm) | 1.1 ± 0.3 | 2.5 ± 0.5 | 2.4 ± 0.5 | <0.0001
Late Lumen Loss (mm) | --- | --- | 0.17 ± 0.49 | ---
Diameter Stenosis (%) | 60.1 ± 10.1 | 14.1 ± 10.9 | 15.0 ± 12.4 | <0.0001
In-Scaffold Analysis |  |  |  | 
Interpolated RVD (mm) | --- | 3.1 ± 0.4 | 2.9 ± 0.4 | <0.0001
MLD (mm) | --- | 2.8 ± 0.4 | 2.5 ± 0.5 | <0.0001
Acute Gain (mm) | --- | 1.6 ± 0.4 | --- | ---
Late Lumen Loss (mm) | --- | --- | 0.27 ± 0.41 | 
Diameter Stenosis (%) | --- | 9.4 ± 5.4 | 13.7 ± 10.89 | 0.0018
Binary Restenosis (%) | --- | --- | 1.6% (1/60) | ---

## Slide 11: Primary Efficacy End Point: Cumulative Frequency Distribution 9-Month In-Scaffold Late Lumen Loss
Chart: Late Lumen Loss (mm) at 9 Months
| -0.25 | -0.14000000000000001 | -0.12 | -7.0000000000000007E-2 | -7.0000000000000007E-2 | -0.05 | -0.03 | -0.03 | -0.01 | 0 | 0.03 | 0.03 | 0.04 | 0.05 | 7.0000000000000007E-2 | 0.08 | 0.1 | 0.1 | 0.11 | 0.12 | 0.12 | 0.13 | 0.14000000000000001 | 0.14000000000000001 | 0.15 | 0.15 | 0.16 | 0.16 | 0.17 | 0.18 | 0.19 | 0.2 | 0.21 | 0.21 | 0.22 | 0.23 | 0.23 | 0.24 | 0.25 | 0.26 | 0.28000000000000003 | 0.31 | 0.32 | 0.32 | 0.34 | 0.34 | 0.36 | 0.37 | 0.4 | 0.44 | 0.53 | 0.56000000000000005 | 0.56999999999999995 | 0.62 | 0.65 | 0.67 | 0.71 | 0.72 | 1.45 | 2.64
Actual Frequency | 0.016667 | 0.033333 | 0.05 | 0.066667 | 0.083333 | 0.1 | 0.11667 | 0.13333 | 0.15 | 0.16667 | 0.18333 | 0.2 | 0.21667 | 0.23333 | 0.25 | 0.26667 | 0.28333 | 0.3 | 0.31667 | 0.33333 | 0.35 | 0.36667 | 0.38333 | 0.4 | 0.41667 | 0.43333 | 0.45 | 0.46667 | 0.48333 | 0.5 | 0.51667 | 0.53333 | 0.55 | 0.56667 | 0.58333 | 0.6 | 0.61667 | 0.63333 | 0.65 | 0.66667 | 0.68333 | 0.7 | 0.71667 | 0.73333 | 0.75 | 0.76667 | 0.78333 | 0.8 | 0.81667 | 0.83333 | 0.85 | 0.86667 | 0.88333 | 0.9 | 0.91667 | 0.93333 | 0.95 | 0.96667 | 0.98333 | 1

## Slide 12: In-Scaffold OCT Measurements
OCT Measurements Mean ± SD (n) | Post-BRS Implantation (n= 55) | 9-Month Follow-Up (n= 60) | Difference (Post vs. 9-Months)
Mean Lumen Area (mm3/mm) | 7.018 ± 1.634 | 6.378 ± 1.932 | -0.64 (-9.1%)
Mean Outer Scaffold Area (mm3/mm) | 7.624 ± 1.563 | 8.093 ± 1.853 | 0.469 (6.2%)
Mean Inner Scaffold Area (mm3/mm) | 6.243 ± 1.390 | 6.683 ± 1.642 | 0.440 (7.0%)
Mean Scaffold Mass (mm3/mm) | 1.380 ± 0.182 | 1.410 ± 0.222 | 0.030 (2.2%)
Percent Tissue Protrusion (%) | 0.3 ± 0.7 | --- | ---
Percent NIH Volume (%) | --- | 8.9 ± 6.9 | ---
Post-Implantation Stent Fracture (%) | 0% | --- | ---
Late Scaffold Discontinuities (# stents, %) | --- | (1) 1.7% | ---
OCT Volumetric Measurements Mean ± SD (n) | Percent Covered Struts (At 9 Months) | Percent Uncovered Struts (At 9 Months) | Total
Percent Apposed per Patient (%) | 94.194 ± 7.082 | 4.136 ± 5.652 | 98.3%
Percent "Malapposed " of Total Struts (%) | 0.591 ± 1.765 | 0.181 ± 0.730 | 0.8%
Percent "Orifice of Branch" of Total Struts (%) | 0.781 ± 1.433 | 0.118 ± 0.277 | 0.9%
Total | 95.6% | 4.4% | 100%

## Slide 13: Safety Endpoints Through 9 Months
Safety Endpoints % (n) | In Hospital (n=63) | Discharge to 30 Days (n=63) | 9 Months (n=61)
Target Vessel Failure (Cardiac Death, TV-MI, or ID-TLR) | 3.2% (2) | 0% | 4.9% (3)
All Death Cardiac Death Non-Cardiac Death | 0% 0% 0% | 0% 0% 0% | 1.6% (1) 0% 1.6% (1)
Target Vessel MI Q-wave MI Non-Q-wave MI | 3.2% (2) 0% 3.2% (2) | 0% 0% 0% | 3.3% (2) 0% 3.3% (2)
Ischemia Driven TLR PCI CABG | 0% 0% 0% | 0% 0% 0% | 1.6% (1) 1.6% (1) 0%
ARC Stent Thrombosis Definite or Probable Possible | 0% 0% | 0% 0% | 0% 0%

## Slide 14: The FORTITUDE Study: Conclusions
The FORTITUDE Study, an international, multi-center investigation of the clinical performance of the 1st generation (150-µm) Amaranth BRS showed:
  High clinical device success rate (98.4%)
  Low MACE rates (4.9%; 2 out 3 events related to peri-procedural MIs)
  Low angiographic binary restenosis (1.6%) and late loss (0.27 ± 0.41 mm)
  High levels of strut coverage (96%) and scaffold stability (1.7% late discontinuities) in OCT at 9-months
Amaranth’s proprietary ultra-high molecular weight PLLA combined with unique polymer processing technology has led to the further miniaturization of the BRS. Two FIH studies are already testing second generation Amaranth’s BRS:
  RENAISANCE II (115-µm BRS): Enrollment complete
  RENAISANCE III (<100-µm BRS): Enrollment already started
Due to the unique polymer features, these future generation scaffolds have the potential to match the biological performance of current metallic DES