## Slide 1: MeRes-1 Study:
Three-year clinical and two-year multimodality imaging outcomes of thin- strut sirolimus-eluting bioresorbable vascular scaffold in patients with coronary artery disease
Dr. Praveen Chandra
MD, DM, FACC, FESC, FSCAI, FAPSIC
Chairman- Interventional Cardiology Medanta-The Medicity, India
On Behalf of MeRes-1 Investigators

## Slide 2: Potential Conflicts of Interest
Speaker's name : Praveen Chandra
☑ I have the following potential conflicts of interest to declare:
Grant/ Research support: Meril Life Sciences

## Slide 3: Why do we Need a New Approach for Coronary Artery Disease?
Pre
Post 5 years
15 years
In-stent restenosis (at 15 years)
Pre
Post
2 years
17 years
Stent thrombosis (at 17 years)
Very late adverse events after metallic stents
Yamaji K et al. Circ CV Int 2010

## Slide 4: Leave no permanent implant behind – Future Tx Possibilities
The Promise of 1st Gen BVS– ‘Golden Tube’

## Slide 5: Initial Results of BVS were promising
Absorb 5-Year Cohort B Presented by Patrick W. Serruys

## Slide 6: But, Reality was presenting differently & we learnt from the same
BVS specific procedures/techniques – lesion selection, dilatation, sizing
2nd Generation device required

## Slide 7: What are we looking from 2nd Generation BRS?
Acute Performance + Long Term Safety and Efficacy
Reduced strut thickness, improved profile for better deliverability
Faster degradation and possibly lower Scaffold Thrombosis Large size matrix to cover multitude of morphologies Ability to treat lesions across clinical spectrum
Regular Cath-lab storage conditions & long shelf life
Source: Data on File; 3year f/up of MeRes100 in Porcine coronary arteries, CRF Skirball Centre for Innovation

## Slide 8: MeRes100 – The 2nd Generation BRS
MeRes100
Cath-Lab Temperature
63 SKUs
D 2.50 – 4.00 mm & L 8-40 mm
Hybrid Geometry
100µm
1.2mm
Couplets of 3 RO markers
on each end
24%
1st Gen BVS
Prefer Refrigeration
14 SKUs
D 2.50-3.50 mm & L 8-28 mm
Multi-link design platform
150µm
1.4mm
Pair of RO markers at
opposite end
35-40%
Features
Cell Design
Strut Thickness
RO Markers
Storage
Size Matrix
Crossing
Profile
Scaffold to
Artery Ratio
Absorb 150μm
100 μm
MeRes100 100μm

## Slide 9: OCT images illustrating the changes of strut core appearance at Day 0 and at 1 , 2 & 3 Years Follow-up
Preserved boxes
Ghost scaffold
Day 0
Day 0
Day 0
1 Year
2 Years
3 Years
Golden tube
Source: MeRes100 in Porcine coronary arteries, CRF Skirball Centre for Innovation
MeRes100 BRS: Evidence of ‘Golden Tube’
Pre-Clinical

## Slide 10: MeRes-1 Study Design
CTRI/2015/04/005706
First-in-Human Safety and Efficacy in Patients with Single, De- novo Coronary Lesion (in up to 2 vessels) treated by a Single MeRes100 Scaffold up to 24mm length in 108 pts
Clinical follow-up
N = 108 30-days 6-months 1-year$ 2-years 3-years
*QCA, IVUS, OCT & CTA follow-up
Diameters Lengths DAPT Rx
– 2.25-4.50 mm
– 13-48 mm
– 1 year
CLINICAL FOLLOW-UP | 108 | 108 | 108 | 108 | 108
ANGIOGRAPHIC FOLLOW- UP | - | 37 | - | 37 | -
OCT FOLLOW-UP | - | 13 | - | 13 | -
IVUS FOLLOW-UP | - | 12 | - | 12 | -
CTA FOLLOW-UP | - | - | 12 | - | -
$Seth A et al., EuroIntervention 2017; 13: 415-423. *Pre-designated sites and patients consents

## Slide 11: Key Eligibility Criteria
Age 18-65 years
Up to 2 lesions in native arteries
1 lesion per target vessel allowed
RVD 2.75-3.50 mm
Lesion length ≤ 20 mm
Stenosis ≥ 50% & < 100%
TIMI ≥ 1
Key Inclusion Criteria Key Exclusion Criteria
Acute MI <7 days
Creatinine ≥1.3 mg/dL
Prior revascularization
LVEF ≤ 30%
LM and/or Ostial location
Significant calcification
Bifurcation lesion (SB >2 mm)
Severe tortuosity/angulation

## Slide 12: Major Endpoints
Safety
  Primary Endpoint:
    MACE at 6-month (Cardiac death, MI*, ID-TLR)
  Secondary Endpoints:
    Device & procedure success
    Scaffold thrombosis (ARC defined)
Efficacy
  QCA: Late lumen loss (in-scaffold / in-segment)
  OCT: Minimum lumen area (flow area), NIH area
  IVUS: Scaffold & lumen area, %VO
  CTA: Mean/minimal lumen, plaque & vessel area; Area stenosis;
% Cross sections with calcified, mixed & non-calcified plaque
* Definition of MI – includes all Myocardial Infarction

## Slide 13: Study Organisation
PI – Dr. Ashok Seth, Fortis Escorts, New Delhi
Co-PI – Dr. Praveen Chandra, Medanta, Gurugram
Co-PI – Dr. Vinay K. Bahl, AIIMS, New Delhi
Core Labs
  Angiographic
  IVUS / OCT /CTA
Cardiovascular Research Center, Sao Paulo
Cardialysis, Rotterdam
CRO
  Data Management – JSS, New Delhi

## Slide 14: Investigating Sites
108 Patients, 13 Investigating Sites
Investigating Site | City | Investigator | # Enrolled
Jayadeva | Bangalore | Dr. C. N. Manjunath | 23
LTMG | Mumbai | Dr. Ajay Mahajan | 20
Max | New Delhi | Dr. Viveka Kumar | 13
SGPGI | Lucknow | Dr. P. K. Goel | 11
Medanta The Medicity | Gurugram | Dr. Praveen Chandra | 10
AIIMS | New Delhi | Dr. Vinay K. Bahl Dr. Sundeep Mishra | 07
Hero DMC | Ludhiana | Dr. G. S. Wander | 07
Fortis Escorts | New Delhi | Dr. Ashok Seth | 06
Apollo | Chennai | Dr. Samuel Mathew Dr. G. Sengottuvelu | 04
Sree Chitra | Trivandrum | Dr. Ajit Kumar V. K. | 03
Fortis Vasant Kunj | New Delhi | Dr. Upendra Kaul | 02
GB Pant | New Delhi | Dr. Vijay Trehan | 01
Apollo Jubilee Hills | Hyderabad | Dr. P. C. Rath | 01

## Slide 15: Baseline Demographics
Clinical characteristics of the patients | n = 108
Age, Years, (mean±SD) | 50.1±8.8
Male, n (%) | 77 (71.3)
Smokers, n (%) | 18 (16.7)
Diabetes mellitus, n (%) | 30 (27.8)
Dyslipidemia, n (%) | 14 (13.0)
Hypertension, n (%) | 45 (41.7)
Previous Myocardial Infarction (>7 days), n (%) | 37 (34.3)
Clinical Presentation, n (%) | 
Stable Angina | 56 (51.9)
Unstable Angina | 37 (34.3)
Silent Ischemia/Asymptomatic | 15 (13.9)
Left ventricular ejection fraction, %, (mean±SD) | 50.6±9.9
Type B1/B2/C Lesions 100% device and 99% procedural succes | s 93.1%

## Slide 16: Cumulative Clinical Outcomes up to 3-year Follow-up
*Death due to Aminophylline-induced anaphylactic shock. @ Myocardial Infarction defined as per WHO criteria. $ ARC defined criteria.
Sustained successful clinical outcomes up to 3 years
Events, n (%) | In-Hospital n =108 | 6-month n =108 | 1-year n = 107 | 2-year n = 107 | 3-year n=107
Cumulative MACE | 0 (0) | 0 (0) | 1 (0.93) | 2 (1.87) | 2 (1.87)
Cardiac Death | 0 (0) | 0 (0) | 0 (0) | 0 (0) | 0 (0)
Myocardial Infarction | 0 (0) | 0 (0) | 0 (0) | 0 (0) | 0 (0)
ID-TLR | 0 (0) | 0 (0) | 1 (0.93) | 2 (1.87) | 2 (1.87)
Non-cardiac death | 0 (0) | 1 (0.93)* | 1 (0.93) | 1 (0.93) | 1 (0.93)
Scaffold Thrombosis | 0 (0) | 0 (0) | 0 (0) | 0 (0) | 0 (0)

## Slide 17: Cumulative Clinical Outcomes up to 3-year Follow-up
Absorb 5-Yr Cohort-B
MeRes-1 Study
Events, n (%) | In- Hospital n =108 | 6-month n =108 | 1-year n = 107 | 2-year n = 107 | 
 |  |  |  |  | 3-year n=107
Cumulative MACE | 0 (0) | 0 (0) | 1 (0.93) | 2 (1.87) | 2 (1.87)
Cardiac Death | 0 (0) | 0 (0) | 0 (0) | 0 (0) | 0 (0)
Myocardial Infarction | 0 (0) | 0 (0) | 0 (0) | 0 (0) | 0 (0)
ID-TLR | 0 (0) | 0 (0) | 1 (0.93) | 2 (1.87) | 2 (1.87)
Non-cardiac death | 0 (0) | 1 (0.93)* | 1 (0.93) | 1 (0.93) | 1 (0.93)
Scaffold Thrombosis | 0 (0) | 0 (0) | 0 (0) | 0 (0) | 0 (0)

## Slide 18: Cumulative Frequency Distribution Curve for In-scaffold Late Lumen Loss
Angio QCA – CRC, Sao Paulo, Brazil

## Slide 19: Paired OCT analysis
IVUS/OCT – Cardialysis, Rotterdam
Characteristic | Post- procedure (n=9) | 6-Month (n=9) | 2- year (n=9) | Friedman p- value
Mean flow area, (mm2) | 7.33±2.28 | 6.99±2.75 | 6.49±2.79 | 0.032
Mean lumen area, (mm2) | 7.69±2.36 | 6.99±2.75 | 6.49±2.79 | 0.008
Minimum lumen area, (mm2) | 6.59±2.12 | 4.99±1.65 | 4.29±2.00 | <0.01
Mean scaffold area, (mm2) | 8.06±2.51 | 8.64±3.05 | 8.39±3.19 | 0.121
Minimum scaffold area, (mm2) | 7.13±2.29 | 7.05±2.02 | 6.29±2.43 | 0.120
Mean strut area, (mm2) | 0.14±0.04 | 0.11±0.03 | 0.06±0.02 | 0.001
Covered struts (%) | - | 98.99±1.59 | 99.24±2.27 | 0.102

## Slide 20: Paired IVUS Analysis
Parameters | Post- procedure (n=10) | 6-month (n=10) | 2- year (n=10) | Friedman p-value
Mean lumen area, (mm2) | 6.17±1.28 | 6.28±1.28 | 5.47±1.50 | 0.30
Minimum lumen area, (mm2) | 5.14±1.19 | 4.88±1.05 | 4.05±1.42 | 0.741
Mean scaffold area, (mm2) | 6.20±1.27 | 6.54±1.29 | 5.94±1.34 | 0.122
Mean vessel area, (mm2) | 12.91±4.05 | 13.05±3.30 | 11.98±3.03 | 0.061
Neointimal hyperplasia area, (mm2) | - | 0.14±0.16 | 0.40±0.35 | 0.002
Volume obstruction (%) | - | 2.59±3.10 | 7.50±6.08 | 0.002
IVUS/OCT – Cardialysis, Rotterdam

## Slide 21: MeRes100 Case + OCT F/up out to 2yrs
MeRes100 3.50 x 19 mm
Post-Procedure
6-month OCT f/up
Data on file at Meril Life Sciences, Pvt. Ltd.
47y/F | Diabetic | Hypertensive | No family history | Non-smoker | Stable angina
Post-Procedure 6-Month FU 2-Year FU
2-Year OCT f/up
MeRes 100 3.50x19

## Slide 22: 2nd Generation BRS holds promise
MeRes100
Absorb
2Y
Data on file at Meril Life Sciences, Pvt. Ltd.
2Y
Absorb 5-Year Cohort B Presented by Patrick W. Serruys

## Slide 23: MeRes100 – Global Clinical Program
1-2. Achieved Primary Objective 3-6. Planning phase.
>5,000 Patients Global Clinical Program
MeRes-11 (n=108)
FiM, Single, denovo lesions. 13 Indian Sites
MeRes100 Global3 (n=2,000) All comers, real world registry. 100 participating sites global.
MeRes-Evolve4 (n=800) RCT MeRes100 Vs XIENCE
30 participating sites global
MeRes100-China5 (n=1,242)
RCT 242:242 MeRes100 Vs XIENCE
+ 800 MeRes100. 1 year MACE, ST
MeRes100-US/JPN6 (n=2,000) RCT MeRes100 Vs XIENCE
1 year MACE, ST
MeRes-1 Extend2 (n=64 Single, denovo lesions 8 Global Sites
^MeRes-1 One-Year Results: Seth A. et al. EuroIntervention 2017;13:415-423
^MeRes-1 Ext presented at EuroPCR’2018
Excellent Clinical Safety & Efficacy | MeRes-1 N=107^ | MeRes-1 Extend N=62 ^
Follow-up | 3-year | 2-year
MACE | 2 (1.87%) | 1 (1.61%)
ST | 0% | 0%
Late Lumen Loss | 2-year 0.24± 0.34 mm | 6-month 0.18±0.31mm

## Slide 24: Conclusion & Future Directions
MeRes-1 trial, the 1st human evaluation of novel 2nd generation MeRes100 BRS with 100µm struts demonstrated high acute success as well as long term clinical success up to 3-year follow-up with very low MACE rate of 1.87% (2, ID-TLR) and Zero Scaffold Thrombosis (ST).
All four imaging modalities are consistent in demonstrating high efficacy of MeRes100 – BRS:
QCA at 2-years: Low late lumen loss (0.24± 0.34 mm)
OCT at 2-years: Virtually complete strut coverage (99.24%)
IVUS at 2- years: Sustained mean flow area and very low %VO (7.50%)
These encouraging results of MeRes-1 study provide the basis for further studies, using a wider range of lengths and sizes in more complex and larger patient population.

## Slide 25: MeRes-1 trial (3 years follow-up) simultaneous publication in EuroIntervention

## Slide 26: MeRes100 (100µm BRS) Sirolimus-Eluting Bioresorbable Vascular Scaffold

## Slide 27: Thank You

## Slide 28: MeRes100 Case with Tapered balloon/delivery system
Patient details:
37 Y/male with CAD
CAG: 100% Occlusion in mid LCX
Focal moderate 50% Stenosis in Prox. LAD
PCI with MeRes100 (3.0-2.5X30mm)
Post-PCI Angio
Pre-PCI Angio
Tapered MeRes100 deployed
Post-PCI OCT
3D OCT View of MeRes100 post-PCI
Data on file at Meril Life Sciences, Pvt. Ltd