## Slide 1
A Prospective, Single-Arm, Multicenter Trial of Catheter-Directed Mechanical Thrombectomy for Intermediate-Risk Acute Pulmonary Embolism:
The FLARE Study
Thomas Tu, M.D.
On behalf of the FLARE Investigators
National PIs: Kenneth Rosenfield, M.D. and Victor Tapson, M.D.
April 27, 2018
1

## Slide 2: Disclosures
Nothing to disclose
2

## Slide 3: Background
Catheter-directed thrombolysis (CDT) has been shown to improve right ventricular function in patients with acute pulmonary embolism (PE)
However, prolonged ICU stay, need for thrombolytic administration, and potential bleeding complications with CDT therapy may limit its broad application
Catheter-directed mechanical thrombectomy is an alternative approach that does not require the use of thrombolytics, but hasn’t yet been widely evaluated for safety and efficacy
3

## Slide 4
George et al. J Thorac Imaging 2014;29:W7-W12)
4
Increased RV/LV Ratio Is An Independent Predictor of PE-Related Mortality
Conclusion:
“Both RV strain on TTE and an increased CT RV/LV diameter ratio are predictors of PE-related 30-day mortality with similar prognostic significance.”

## Slide 5: Increased RV/LV Ratio Is An Independent Predictor of PE-Related Mortality
Trujillo-Santos J, et al. J Thromb Haemost 2013;11: 1823-1832
5
Conclusion
“…RVD assessed by CT showed an association with an increased risk of mortality in patients with hemodynamically stable PE…”

## Slide 6: CTA-Derived RV/LV Ratio Is Reproducible and Reliable
Methodology:
The RV/LV ratio was measured in three-dimensional (3D) reformatted reconstructions, adjusting the axial, coronal, and sagittal planes to view the largest diameter of each ventricle as measured perpendicular to the interventricular septum.
Conclusion:
“The reliability of CTA for PE was excellent for the axial and multiplanar reformatted methods for quantifying the right-to-left ventricular ratio…”
Ouriel et al. Vascular Online First, published on April 18, 2016 as doi:10.1177/1708538116645056
6

## Slide 7: FlowTriever System
FlowTriever Device (“FT”)
Aspiration Guide Catheter (“AGC”)
Retraction Aspirator (“RA”)
Navigates through the right heart and delivers FT device to the pulmonary artery
Large bore catheter maximizes aspiration and collection of thrombus
Deployed out of AGC and into thrombus
Disrupts, engages and moves large volume of thrombus
  Retracts the FT with thrombus into the AGC
  Synchronizes aspiration and retrieval
Disruption, maceration and retrieval of clot
Increased lumen
Rapid flow restoration Reduced PA pressure Reduced RV strain
7

## Slide 8: FLARE Study Overview
Objective
  Evaluate the safety and effectiveness of the FlowTriever System for use in the removal of emboli from the pulmonary arteries in the treatment of acute PE
Study Design
  Prospective, single-arm, multicenter study
  106 patients, 18 sites
  Follow-up at 48-hours & 30-days
  Primary endpoints
    Effectiveness – reduction in RV/LV ratio at 48-hours
    Safety – Composite major adverse event rate
8

## Slide 9: Major Adverse Event Definition
Device-related death
Major bleeding (VARC-2 definition)
Treatment-related adverse events:
  Clinical Deterioration
  Pulmonary vascular injury
  Cardiac injury
All endpoints are measured within 48 hrs ± 8 hours

## Slide 10: Study Flow
Baseline
Index Procedure
48-Hour Follow-up
30-Day Follow-Up/ Exit
10
FLARE was an Investigational Device Exemption (“IDE”) study with all appropriate controls including:
Data Safety and Monitoring Board
Clinical Events Committee
Independent Core Lab adjudication of RV/LV ratio for primary effectiveness endpoint
  (Syntactx, LLC, New York, NY, USA)

## Slide 11: Patient Selection
11
Main Inclusion Criteria:
Age ≥ 18 and ≤ 75 years
CTA evidence of proximal PE
PE symptom duration ≤ 14 days
RV/LV ratio of ≥ 0.9
Systolic BP ≥ 90 mmHg
Stable heart rate < 130 bpm

## Slide 12: Patient Selection
12
Main Exclusion Criteria:
Thrombolytic use within 30 days
PHTN with peak PA pressure > 70 mmHg
Vasopressor requirement after fluids to keep pressure ≥ 90 mmHg
FiO2 requirement > 40% room air or > 6 LPM to keep O2 sat > 90%
Hematocrit < 28%, platelets < 100,000/µL, serum creatinine > 1.8 mg/dL, INR > 3
Cardiovascular or pulmonary surgery within 7 days
Actively progressing cancer
Pregnancy
Note: No specific exclusion for increased bleeding risk

## Slide 13: Study Enrollment: April 2016 to October 2017
Chart: 
| Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct
Expected | 0 | 1 | 4 | 7 | 10 | 13 | 16 | 20 | 25 | 31 | 38 | 46 | 55 | 65 | 75 | 85 | 95 | 105 | 105
Actual | 1 | 1 | 4 | 9 | 13 | 14 | 14 | 19 | 22 | 26 | 29 | 42 | 52 | 67 | 86 | 94 | 100 | 103 | 106
13

## Slide 14: Subject Disposition
14

## Slide 15: Baseline Characteristics
# Sites | 18
# Patients treated | 106
Mean age ± SD, years | 55.6 ± 13.6
Mean BMI ± SD, kg/m2 | 36.1 ± 9.5
Male gender, n (%) | 58 (54.7)
Race/Ethnicity, n (%) | 
Caucasian | 87 (82.1)
African American | 18 (17.0)
Hispanic | 1 (0.9)
15

## Slide 16: Comorbidities
 | n/106 (%)
Hypertension | 60 (56.6)
Coronary Artery Disease | 10 (9.4)
Congestive Heart Failure | 6 (5.7)
PFO / Other Shunt | 4 (3.8)
COPD | 8 (7.5)
Chronic Renal Insufficiency | 9 (8.5)
Concurrent DVT | 73 (68.9)
Prior Stroke / TIA | 10 (9.4)
Prior DVT | 14 (13.2)
Prior PE | 10 (9.4)
Recent Surgery – Ortho (4), CV (1*), Urologic (1) | 6 (5.7)
*>7 days
16

## Slide 17: PE Characteristics
 | n/N (%)
sPESI | 
0 | 59/106 (55.7)
1 | 47/106 (44.3)
Elevated Cardiac Troponin | 60/101 (59.4)
Elevated D-Dimer | 45/60 (75.0)
Elevated B-Natriuretic Peptide | 65/89 (73.0)
PE Location | 
Unilateral | 5/106 (4.7)
Central | 5/106 (4.7)
Bilateral | 54/106 (50.9)
Bilateral + Central | 42/106 (39.6)
17

## Slide 18: Procedural Characteristics
Pre-procedure anticoagulation, n (%) | 
UFH | 88 (83.0)
LMWH | 22 (20.8)
Other – VKA (1), NOAC (5) | 6 (5.7)
Right femoral access, n (%) | 101 (95.3)
Received lytics during procedure, n (%) | 2 (1.9)
Mean # devices used | 1.7
Mean # passes | 3.9 ± 1.7
Mean procedure time (min; max) | 1 hr 39 mins (39 mins; 3 hrs 11 mins)
Technical complications (delivery, deployment OR retraction) | 0
18

## Slide 21: FlowTriever Clot Retrieval Experience, Acute to Chronic
21
ACUTE CHRONIC

## Slide 22: RV/LV Ratio Outcomes
Chart: RV/LV Ratio All Patients (N=106)
| Baseline | 48-Hour
 | 1.5306 | 1.1505
 | Baseline | 48 Hour | Reduction | p
All Patients (N=106) | 1.53 | 1.15 | 0.39 | p <0.0001
All Paired Patients (N=103) | 1.54 | 1.15 | 0.39 | p <0.0001
Paired Patients w/o Lytic (N=101) | 1.54 | 1.15 | 0.38 | p <0.0001
Reduction 0.39
p <0.0001
22

## Slide 23: Clinical Outcomes
ICU stay post-procedure, median | 1 day
ICU stay: distribution | 0 = 44 1 = 23 2 = 18 3+ = 21
Days to discharge post-procedure, median | 3 days
# Patients lost-to-follow-up | 2
# Patients any-cause mortality | 1
# MAEs* | 4 (ITT 3.8% , mITT 3.8%)
23

## Slide 24: Major Adverse Events
No intracranial hemorrhage
No access-site major bleeding
No device-related death
No device-related pulmonary injury
No device-related cardiac injury
One patient had a bleeding event
Three patients had treatment-related clinical deterioration

## Slide 25: Major Adverse Events
*MAE Subject # | * MAE Description
#0404 | Hemoptysis, hemothorax, pulmonary infarction; lower lobectomy; possible reperfusion injury
#0808 | Worsening PE, surgical embolectomy
#2101 | Cardiogenic shock, acute respiratory insufficiency
#2422 | Patient agitated during procedure despite sedation; respiratory arrest with VFIB and cardioversion

## Slide 26: FLARE Effectiveness in Context
 | N | Treatment | tPA | Reduction in RV/LV Ratio at 48 Hours
FLARE | 104 | FlowTriever mechanical thrombectomy | 0 mg | 0.39 / 25%
SEATTLE II (2015) | 150 | USAT | 24 mg | 0.42 / 24%
ULTIMA (2014)* | 30 | USAT arm | 10-20 mg | 0.29 / 22%
Becattini et al (2010) | 28 | Systemic Thrombolytic | 30-50 mg | 0.31 / 24%
Fasullo et al (2011) | 35 | Systemic Thrombolytic | 100 mg | 0.40 / 27%
Mi et al (2013) | 57 | Systemic Thrombolytic | 50 mg | 0.11 / 8%
26
*RV/LV Ratio in ULTIMA measured at 24 hours

## Slide 27: FLARE Safety in Context
Study | Major Bleeding | Intracranial Hemorrhage (Fibrinolysis Group)
FLARE | 1/106 (.9%) | 0/106 (0%)
ULTIMA (USAT arm) (Kucher, et al. 2013) | 0/30 (0%) | 0/30 (0%)
PEITHO (tPA arm) (Meyer G, et al. 2014) | 58/506 (11.5%) | 10/506 (2%)
SEATTLE II (Piazza G, et al. 2014) | 17/150 (11.4%) | 0/150 (0%)
27

## Slide 28: Conclusions
Catheter-directed mechanical thrombectomy using the FlowTriever System, without the use of thrombolytics, is safe and effective in improving RV function in patients with intermediate-risk PE
Additionally, it has the potential to reduce bleeding complications and reduce total hospital and ICU length of stay
This study establishes mechanical thrombectomy for acute pulmonary embolism as a viable alternative to thrombolytic-based catheter-directed therapy and warrants further investigation
28

## Slide 29: FLARE Investigators
Thomas Tu, M.D.
Christopher Adams, M.D.
Wissam Jaber, M.D.
Rohit Bhatheja, M.D.
Mitchell Silver, M.D.
Sameer Khandhar, M.D.
Rohit Amin, M.D.
Mitchell Weinberg, M.D.
Tod Engelhardt, M.D.
Eric Peden, M.D.
Robert Maholic, M.D.
David Holmes, M.D.
Scott Lilly, M.D.
Catalin Toma, M.D.
Hussam Hamdalla, M.D.
Glenn Hoots, M.D.
Victor Tapson, M.D.
Monica Hunter, M.D.
National PIs: Kenneth Rosenfield, M.D. and Victor Tapson, M.D.
29

## Slide 30: Backup Slides For Reference Only
30

## Slide 31: Protocol Deviations
Major Protocol Deviations | # of Events | # (%) of Subjects
Total | 40 | 35 (33.0%)
Ineligible subject enrolled | 1 | 1 (0.9%)
Informed consent not obtained/signed/dated | 0 | 0 (0.0%)
Missing Assessment Prescribed by Protocol | 3 | 3 (2.8%)
Assessment Performed Outside Protocol Window | 7 | 7 (6.6%)
Visit Performed Outside Protocol Window | 29 | 27 (25.5%)
31

## Slide 32: Limitations
The single-arm study design precluded direct comparison with the efficacy and safety of systemic fibrinolysis or anticoagulation alone.
Our study design did not allow for evaluation of clinical end points such as hemodynamic collapse or mortality.
32

## Slide 33: Poolability – RV/LV Analysis No Evidence in Heterogenity Across Sites
Analysis | Pseudo-Site[1] | N | Mean (SE) | P-value
ANOVA of Change in RV/LV Ratios from Baseline to 48-hour | A | 5 | 0.44 (0.09) | 
 | B | 6 | 0.27 (0.07) | 
 | C | 6 | 0.33 (0.08) | 
 | D | 3 | 0.55 (0.20) | 
 | E | 26 | 0.34 (0.06) | 
 | F | 7 | 0.42 (0.11) | 
 | G | 6 | 0.53 (0.15) | 
 | H | 9 | 0.38 (0.11) | 
 | I | 8 | 0.41 (0.08) | 
 | J | 25 | 0.39 (0.05) | 0.85
[1] Pseudo-Sites Key: A = {2, 3, 5, 7, 12}; B = {10, 13, 15}; C = {16, 18}; D = {20, 21}; E = {4}; F = {8}; G = {9}; H = {11}; I = {14}; J = {24}.
33

## Slide 34: FLARE vs. SEATTLE II
 | FLARE | SEATTLE II
Interventional Device | FlowTriever | EKOS
Design | Single arm OPC, Prospective, IDE | Single arm OPC, Prospective, IDE
Patients / Sites | 106 patients / 18 sites | 150 patients / 22 sites
Safety Endpoints | 1 Composite MAE at 48-Hours = 3.8% (n=4) 2 30-Day Mortality = 0.9% (n=1) | 1 Major Bleeding at 72-Hours = 10% (n=15) 2 30-Day Mortality = 2.7% (n=4)
Primary Efficacy Endpoint | Reduction in RV/LV ratio at 48 hours: 0.39 / 25% (n=106; OPC = >0.12) | Reduction in RV/LV ratio at 48 hours: 0.42 / 24%
ICU Stay | Median = 1 day % patient w/ ICU stay = 58% (n=62) | % patients w/ ICU stay = 100%
Length of Hospital Stay | Mean = 4.1 days Median = 3 days | Mean = 8.8 days
Device Metrics | Mean # FT devices/case = 1.7 Mean # passes/case = 3.9 | Mean total dose tPA = 24 mg
34

## Slide 35: FLARE vs. SEATTLE II
 | FLARE | SEATTLE II
Key Inclusion Criteria | Age ≥18 and ≤75 RV/LV ≥0.9 PE symptom duration ≤14 days SBP ≥90 mmHg Stable HR <130 BPM | Age ≥18 RV/LV ≥0.9 PE symptom duration ≤14 days Massive PE (syncope, systemic arterial hypotension, cardiogenic shock, or resuscitated cardiac arrest) Submassive PE (RV dysfunction)
Key Exclusion Criteria Similarities | Major CV or pulmonary surgery within 7 days Hematocrit <28% Creatinine >1.8 mg/dL Vasopressor requirement keep pressure >90 mmHg Use of lytic within 30 days of enrollment | Major surgery within 7 days Hematocrit <30% Creatinine >2.0 mg/dL SBP <80 mmHg despite vasopressor or inotropic support Use of lytic/GP IIb/IIIa antagonists within 3 days of enrollment
Key Exclusion Criteria Differences | Peak PAP >70 mmHg FiO2 requirement >40%/6 LPM keep O2 sat >90% | Stroke or TIA within 1 year Head trauma within 1 year Other active intracranial or intra-spinal disease within 1 year Recent active bleeding from a major organ Clinician deemed subject at high risk for catastrophic bleeding
35

## Slide 36: ###
36