## Slide 1: Pulsed Field Ablation Treatment in Paroxysmal and Persistent Atrial Fibrillation Patients: Acute and Long-term Outcomes from the PULSED AF Pivotal Trial
Dr. Atul Verma
On behalf of the PULSED AF Investigators
@atulverma_md

## Slide 2: Disclosures
Company Medtronic Biosense Webster Biotronik
Bayer
Kardium Medlumics
Relationship
Consultant/ Honoraria/ Research grant
Consultant/ Honoraria/ Research grant Research grant
Research grant/ Honoraria Consultant
Consultant/ Honoraria
The PULSED AF study (NCT04198701) was funded by Medtronic, Inc.
Reference materials were requested and obtained from Medtronic, Inc. for portions of this presentation.
The Medtronic PulseSelectTM PFA system is investigational, not approved in the US.
The following data and analyses have not been reviewed by any regulatory bodies, including FDA.

## Slide 3: Introduction
Catheter ablation is an effective treatment for patients with symptomatic, drug-refractory atrial fibrillation.1,2
Thermal modes of ablation are limited by the potential for collateral tissue damage.3
Pulsed field ablation creates lesions in cardiac tissue non-thermally through the mechanism of irreversible electroporation (IRE).4,5
IRE involves tissue exposure to high electric field gradients, inducing cell membrane hyper-permeabilization within milliseconds, leading to cell death.6
Calkins H et al. Europace. 2018;20:e1-e160
Hindricks G et al. Eur Heart J. 2021;42:373-498.
Cappato R et al. Circ Arrhythm and Electrophysiol. 2010;3:32-38
Stewart MT et al. J Cardiovasc Electrophysiol. 2021;32:958-969.
Yarmush ML et al. Annu Rev Biomed Eng. 2014;16:295-320.
Kotnik T et al. Annu Rev Biomed Eng. 2019;48:63-91.

## Slide 4
One application = 4 bipolar, biphasic trains lasting 100-200 ms, 2800-3000 V peak to peak

## Slide 5: PULSED AF Study Design
PULSED AF: prospective, global, multi-center, non-randomized paired single-arm trial
Key Inclusion Criteria
Prior antiarrhythmic drug failure
Diagnosis of recurrent symptomatic paroxysmal or persistent AF
18-80 years old
Key Exclusion Criteria
Long-standing persistent AF (continuous AF that is sustained >12 months)
Left atrial diameter > 5.0 cm
Prior left atrial ablation or surgery
Patient not on oral anticoagulation therapy for at least 3 weeks prior to procedure
41
Centers
67
Operators
9
Countries
150
Paroxysmal AF
150
Persistent AF
Patients underwent pulmonary vein isolation using the PulseSelectTM Pulsed Field Ablation System and were followed for 12 months

## Slide 6: Primary Efficacy Endpoint
Freedom from a composite endpoint of acute procedural failure, arrhythmia recurrence, repeat ablation, direct current cardioversion, left atrial surgery, or antiarrhythmic drug escalation through 12 months (excluding a 90-day blanking period)
Pre-Specified Performance Goal: >50% (paroxysmal) or >40% (persistent) at 12 months
All cardiac monitoring was adjudicated by an independent core laboratory
Cardiac Monitoring During Follow-up
 | 1-M | 2-M | 3-M | 4-M | 5-M | 6-M | 7-M | 8-M | 9-M | 10-M | 11-M | 12-M
TTM |  |  |  | Weekly and symptomatic transmissions |  |  |  |  |  |  |  | 
ECG |  |  | X |  |  | X |  |  |  |  |  | X
HM |  |  |  |  |  | X |  |  |  |  |  | X
 | Blanking period |  |  | Post-blanking period |  |  |  |  |  |  |  | 

## Slide 7: Primary Safety Endpoint
Freedom from a composite of serious procedure and device-related adverse events
Pre-Specified Performance Goal: <13%
All primary safety endpoint events were adjudicated by an independent clinical events committee

## Slide 8: Patient Flow Diagram
96% of patients reached 12-month follow-up
Enrolled: 383
Paroxysmal AF
(n = 200)
Persistent AF
(n = 183)
14 Not Ablated:
-Screen failure (4)
-Physician decision (3)
-Withdrawal by patient (3)
-Protocol deviation (1)
-Sponsor request (1)
-Other (2)
9 Not Ablated:
-Screen failure (5)
-Procedure not
attempted (3)
-Sponsor request (1)
150 Primary Cohort
150 Primary Cohort
36 Roll-In Patients
24 Roll-In Patients

## Slide 9: Results: Patient Baseline Characteristics
Patient Characteristics Paroxysmal (n = 150) Persistent (n = 150)
Male Sex 64% 75%
Age (years) 63.4 ± 9.9 66.0 ± 9.0
Left Atrial Diameter (mm) 38.7 ± 5.8 42.0 ± 5.0
Left Ventricular Ejection Fraction (%) 60.3 ± 4.8† 57.6 ± 6.4
Years Since AF Onset 3.8 ± 6.2 2.7 ± 3.7
Number of Failed Antiarrhythmic Drugs 1.3 ± 0.6 1.3 ± 0.6
Cardioversions Prior to Enrollment
Electrical Pharmaceutical
22%
10%
62%
7%
Body Mass Index (kg/m2) 28.6 ± 5.9 30.9 ± 6.8
Medical History
Stroke
Transient ischemic attack
Myocardial infarction
Coronary artery disease
Hypertension
Obstructive sleep apnea
Valve dysfunction
3% 2%
1% 2%
5% 5%
21% 21%
49% 65%
20% 31%
15% 11%
16% 14%
Diabetes
CHA2DS2VASc 1.8 ± 1.4 2.1 ± 1.4
Data represented as mean ± SD or percentage; †n=149

## Slide 10: Procedural Characteristics
Type of anesthesia used – no. (%) |  | 
General anesthesia | 89% | 84%
Deep sedation | 5% | 7%
Conscious sedation | 5% | 9%
Neuromuscular Blockade Use | 5% | 7%
Intra-procedural Cardioversions | 17% | 65%
Max esophageal temperature change from baseline (°c) | 0.3 (0.1-0.5) § | 0.2 (0.0-0.5) ǁ
Mapping / Navigation system used – no. (%) CARTO | 26% | 23%
EnSite | 57% | 59%
Rhythmia | 11% | 10%
None | 5% | 8%
Parameter Paroxysmal (n = 150) Persistent (n = 150)
Acute Pulmonary Vein Isolation
100% 100%
Skin-to-skin Procedure Time (min)*
Device Left Atrial Dwell Time (min)†
125 (102-157) 133.5 (107-173)
58.5 (46-76) 62.5 (51-84)
Time Between First and Last Application
Fluoroscopy Time (min)
Total pulsed field ablation energy delivered (sec)
Number of applications per procedure
53 (40-68) 60 (45-77)
21 (15-31) 23 (14-38)
23 (19-28) 27 (23-34)
43.5 (37-54) 52.5 (44-67)
Data represented as median (IQR) or percentage; *First sheath in, to last sheath out; †Includes protocol-mandated 20-minute wait period and post-ablation mapping
§Data were available for 67 patients; ǁData were available for 73 patients.

## Slide 11: Primary Efficacy Results Freedom from a composite endpoint of acute procedural failure, arrhythmia recurrence, repeat ablation, direct current cardioversion, left atrial surgery, or antiarrhythmic drug escalation through 12 months (excluding a 90-day blanking period)
Both paroxysmal and persistent atrial fibrillation cohorts met predetermined effectiveness performance goals.
Paroxysmal Atrial Fibrillation
Persistent Atrial Fibrillation

## Slide 12: Freedom from AT/AF/AFL
Paroxysmal Atrial Fibrillation
Persistent Atrial Fibrillation
Freedom from atrial arrhythmia recurrence at 12 months was 69.5% in the paroxysmal and 62.3% in the persistent atrial fibrillation cohort

## Slide 13: Clinical Success
Paroxysmal Atrial Fibrillation
Persistent Atrial Fibrillation
Freedom from symptomatic recurrence is based on trans-telephonic monitoring only
Clinical success was defined as freedom from symptomatic atrial arrhythmia recurrence at 12 months

## Slide 14: Primary Safety Results
Number with a Primary Safety Event
Primary Safety Event Within 6 months | Paroxysmal AF (n = 150) | Persistent AF (n = 150)
Pulmonary vein stenosis (>70% diameter reduction) | 0 | 0
Phrenic nerve injury/diaphragmatic paralysis ongoing at 6 months | 0 | 0
Atrioesophageal fistula | 0 | 0
Within 30 days |  | 
Cardiac tamponade/perforation | 0 | 1
Cerebrovascular accident | 1 | 0
Transient ischemic attack | 0 | 0
Major bleeding requiring transfusion | 0 | 0
Myocardial infarction | 0 | 0
Pericarditis requiring intervention | 0 | 0
Vagal nerve injury resulting in esophageal dysmotility or gastroparesis | 0 | 0
Vascular access complications requiring intervention | 0 | 0
Death | 0 | 0
PFA system- or procedure-related cardiovascular and pulmonary adverse event prolonging/requiring hospitalization >48 hours (excluding recurrent AF/AFL/AT) | 0 | 0
0.7% safety event rate in each cohort
Both paroxysmal and persistent atrial fibrillation cohorts met predetermined safety performance goals (<13%, p=0.002)
)

## Slide 15: Quality of Life
60.4
89.8
100
80
60
40
20
0
Mean AFEQT score
62.0
91.0
60
40
20
0
80
100
Mean AFEQT score
Paroxysmal AF
Persistent AF
0.86
0.91
0
0.2
0.4
0.6
1
0.8
Mean EQ-5D-5L
score
0.86
0.92
0.6
0.4
0.2
0
0.8
1
Mean EQ-5D-5L
score
+29.4 (p<0.0001)
Quality of life measures indicate a clinically meaningful improvement1-3
AFEQT EQ-5D-5L
22% more patients were not anxious or depressed at 12 mo vs. baseline
11% more patients had no problems doing their usual activities at 12 mo vs. baseline
19% more patients were not anxious or depressed at 12 mo vs. baseline
21% more patients had no problems doing their usual activities at 12 mo vs. baseline
1, Dorian P et al. Am Heart J. 2013;166:381-
387.e388.
2, Holmes DN et al. Circ Cardiovasc Qual Outcomes. 2019;12:e005358.
3, Coretti S et al. Expert Rev Pharmacoecon Outcomes Res. 2014;14:221-233.
Baseline
12 Months
+29.0 (p=0.001)
+0.05 (p<0.0001)
+0.06 (p<0.0001)
Baseline
12 Months
Baseline
12 Months
Baseline
12 Months

## Slide 16: PV Stenosis Sub-Study
 |  | Pulmonary Vein Diameter Change | 
Vein | N* | Moderate Change no. (%)1 | Severe Change no. (%)2
All | 275 | 0 (0) | 0 (0)
RIPV | 63 | 0 (0) | 0 (0)
RSPV | 62 | 0 (0) | 0 (0)
RMPV | 9 | 0 (0) | 0 (0)
LIPV | 63 | 0 (0) | 0 (0)
LSPV | 63 | 0 (0) | 0 (0)
LCPV | 15 | 0 (0) | 0 (0)
No moderate or severe stenosis was observed in 275 pulmonary veins on cardiac computed tomography or MRI imaging at 3 months
Pulmonary Vein Stenosis Sub-Study
150-70% reduction, 1≥70% reduction.

## Slide 17: Cerebral MRI Sub-Study
Cohort | Number of Patients | Silent Cerebral Lesions -- no. (%)
Paroxysmal AF | 26 | 2 (8)
Persistent AF | 19 | 2 (11)
Total | 45 | 4 (9)
New silent cerebral lesions were observed in 4 of 45 patients (9%) undergoing cerebral MRI at baseline and within 72 hours post-ablation
Cerebral MRI Sub-Study

## Slide 18: Conclusion
Primary safety endpoint rate of 0.7% observed for both cohorts
  No occurrence of phrenic, esophageal, pulmonary vein injury, or coronary artery spasm
  Both paroxysmal and persistent atrial fibrillation cohorts met predetermined safety performance goals (<13%)
Acute isolation was demonstrated in 100% of all pulmonary veins
Both paroxysmal and persistent atrial fibrillation cohorts met predetermined effectiveness performance goals
  66.2% freedom from a primary efficacy endpoint event in paroxysmal AF patients
  55.1% freedom from a primary efficacy endpoint event in persistent AF patients
Pulsed field ablation resulted in a clinically meaningful improvements in quality of life
Pulsed field ablation resulted in 79.7% (paroxysmal) and 80.8% (persistent) clinical success

## Slide 19: PULSED AF Committees
Steering Committee
Dr. Atul Verma
Dr. Lucas V.A. Boersma Dr. Hugh Calkins
Dr. Prashanthan Sanders Dr. David E. Haines
Dr. Francis E. Marchlinski Dr. Andrea Natale
Dr. Gerhard Hindricks
Dr. Douglas L. Packer Dr. Karl-Heinz Kuck
Southlake Regional Health Center, Toronto, Canada
St Antonius Hospital, Nieuwegein, Netherlands Johns Hopkins Hospital, Baltimore, MD
Univ of Adelaide & Royal Adelaide Hospital, Adelaide, Australia Beaumont Health, Royal Oak, MI
Hospital of the Univ of Pennsylvania, Philadelphia, PA Texas Cardiac Arrhythmia Institute, Austin, TX
Heart Center - University of L, Leipzig, Germany
Mayo Clinic-St. Mary`s Hospital, Rochester, MN LANS Cardio, Hamburg, Germany
Clinical Events Committee
Dr. Wendy Tzou Dr. Pierre Fayad Dr. Peter Friedman
Dr. Melissa Robinson
Dr. Jonathan Steinberg
Data Monitoring Committee
Dr. George Crossley Dr. Timothy Church Dr. Daryl Gress
Dr. Carina Blomström-Lundqvist
Dr. Stephan Willems Dr. Jeanne Poole

## Slide 20: PULSED AF Investigators
Principal Investigator Site Name
David DeLurgio (co-author) Emory Saint Joseph's Hospital (Atlanta GA)
Nitesh Sood (co-author) Southcoast Health System
Hiroshi Tada (co-author) University of Fukui Hospital
Robert Hoyt Iowa Heart Center
Andrea Natale Texas Cardiac Arrhythmia Research Foundation
James Irwin BayCare Medical Group Cardiology
David Haines Beaumont Health System
Suneet Mittal The Valley Hospital
Sarfraz Durrani MedStar Washington Hospital Center
Robert Sangrigoli Doylestown Health Cardiology
Luigi Di Biase Montefiore Medical Center
Oussama Wazni Cleveland Clinic
Atul Verma Southlake Regional Health Centre
Jose Osorio Grandview Medical Center
Teiichi Yamane The Jikei University Hospital
Tetsuo Sasano Tokyo Medical and Dental University Hospital
Hirofumi Tomita Hirosaki University Hospital
Sanjaya Gupta St. Luke's Mid America Heart Institute
Helmut Friedrich Pürerfellner Ordensklinikum Linz GmbH / Elisabethinen
Francis E Marchlinski Hospital of the University of Pennsylvania
Lucas V. A. Boersma St. Antonius Ziekenhuis
Hugh Calkins The Johns Hopkins Hospital
Principal Investigator
Bradley Knight
Site Name
Northwestern University
Mattias Duytschaever AZ Sint-Jan Brugge-Oostende av
Larry Chinitz NYU Langone Medical Center
John Rhyner Mission Hospital
Ángel Arenal Maiz Hospital General Universitario Gregorio Marañón
Ethan Ellis Medical Center of the Rockies
Jason Andrade Vancouver General Hospital
J. Michael Mangrum University of Virginia Medical Center
Bradley Wilsmore John Hunter Hospital
Alexandre Zhao CMC - Clinique Ambroise Paré
Raman Mitra Northwell Health
Alefiyah Rajabali Providence Saint Vincent Medical Center
Sandeep Jain University of Pittsburgh Medical Center
Andre Gauri Spectrum Health
Peter Noseworthy Mayo Clinic (Rochester MN)
Jean-Francois Sarrazin
Darryl Wells
John Hummel
Prashanthan Sanders
Vidal Essebag McGill University Health Centre (MUHC)
Institut Universitaire de Cardiologie et de Pneumologie de Québec
Swedish Medical Center
The Ohio State University Heart and Vascular Research Organization
Royal Adelaide Hospital

## Slide 21: Thank you to all PULSED AF investigators and all patients
On behalf of Dr. Atul Verma and the PULSED AF steering committee
@atulverma_md

## Slide 22: Announcing publication release: