## Slide 1: LAA Closure with the Amulet Device
Sameer A. Gafoor, MD
1Swedish Heart and Vascular: Ming Zhang, Paul Huang, Darryl Wells, Adam Zivin, Eric Williams,
John Petersen II, Madalena Petrescu, Nimish Muni, Robert Bersin, Eric Lehr, Sam Youssef, Glenn Barnhart, Irina Penev, Amanda Ray, Cale Peterson, Julia Antonyuk, Thearry Deap, Zachary Newhart,
2CVC Frankfurt: Jennifer Franke, Simon Lam, Stefan Bertog, Laura Vaskelyte,
Ilona Hofmann, Markus Reinartz, Horst Sievert
Swedish Heart and Vascular: Swedish Medical Center, Seattle, WA, USA
CVC: CardioVascular Center Frankfurt, Frankfurt, Germany

## Slide 2
Disclosure Statement of Financial Interest
Within the past 12 months, I or my spouse/partner have had a financial interest/arrangement or affiliation with the organization(s) listed below.
Affiliation/Financial Relationship
Company
Grant/Research Support
Consulting Fees/Honoraria
Boston Sci, Abbott Vasc, Medtronic
Boston Sci, Abbott Vasc, Medtronic

## Slide 3: Topics
Device
Case
Data

## Slide 4: Amplatzer Cardiac Plug
Lobe diameter 16-30mm
Lobe length 6.5mm
Disk diameter 20-36mm
9, 10 or 13F sheath

## Slide 5: Amulet
Pre-loaded
Recessed end screw
Larger disc diameter
Longer lobe length
Longer waist length
Larger sizes up to 34mm
Stiffer stabilizing wires (.0065)
More stabilizing wires on larger devices

## Slide 6: Recessed End Screw
Recessed end screw creates a uniform surface in the left atrium
90 days — Preclinical canine model
Notes: The end screw on the Amulet™ device, where the delivery cable is attached to the implant, has been recessed. By eliminating the protruding end screw, this change is intended to create a more uniform surface in the left atrium once the device has been released.

## Slide 7: Stabilizing Wire Changes
Number of stabilizing wires dependent on lobe diameter
Designed to increase stability of the lobe inside the left atrial appendage
AMPLATZER™ Cardiac Plug
Sizes 16 – 30 mm: 6 pairs
Amulet™ Device
Sizes 16 – 18 mm: 6 pairs
Sizes 20 – 25 mm: 8 pairs
Sizes 28 – 34 mm: 10 pairs
Notes: For the Amulet™ device, the number of stabilizing wires is dependent on the diameter of the lobe. In larger sized Amulet devices, the number of stabilizing wires has been increased. This was done to make the gap between stabilizing wires more consistent across the entire size range, and increase the overall stability of the Amulet device particularly among the larger sizes.

## Slide 8: Device Specifications
Feature | AMPLATZER™ Amulet™ |  |  |  |  |  |  |  | AMPLATZER™ Cardiac Plug |  |  |  |  |  |  |  | 
Size / Lobe Diameter (mm) | 16 | 18 | 20 | 22 | 25 | 28 | 31 | 34 | 16 | 18 | 20 | 22 | 24 |  | 26 | 28 | 30
Disc Diameter | Lobe + 6 mm |  |  |  | Lobe + 7 mm |  |  |  | Lobe + 4 mm |  |  |  | Lobe + 6 mm |  |  |  | 
Lobe Length | 7.5 mm |  |  |  | 10 mm |  |  |  | 6.5 mm |  |  |  |  |  |  |  | 
Waist Length | 5.5 mm |  |  |  | 8 mm |  |  |  | 4 mm |  |  |  |  |  |  |  | 
Stabilizing Wires | 6 pairs |  | 8 pairs |  |  | 10 pairs |  |  | 6 pairs |  |  |  |  |  |  |  | 
Sheath Diameter | 12F 14F (with Adaptor) |  |  |  |  | 14F |  |  | 9F | 10F |  |  |  | 13F |  |  | 
Notes: The AMPLATZER™ Amulet™ has undergone several dimensional changes in relation to the AMPLATZER™ Cardiac Plug.
The lobe diameter now has a range from 16mm to 34mm, allowing device implantation in larger appendages.
The disc diameter has been increased slightly to allow for better coverage of the LAA orifice.
The lobe length has been increased to 7.5mm on the smaller devices and 10mm on the larger devices. This allows the lobe to get more surface contact with the left atrial appendage, and is intended to improve the overall stability of the implant.
The waist length of the device has also been increased. This allows for more flexibility in identifying the appropriate landing zone and positioning the lobe in more challenging or anatomies, while still allowing the disc to fully cover the LAA orifice.
The sheath sizes used for the Amulet™ device are 12 French and 14 French. There is also an adaptor supplied with the Amulet device which will allow the 14 French sheath to be used with all device sizes, depending on operator preference.

## Slide 9
Ball position
Counterclokckwise rotation
Deployment of lobe
D. Deployment of disc
E. Device stability evaluation
F. Gentle tug test

## Slide 10
Yellow and red marks the device
Red and white marks the mitral valve

## Slide 11: Five Signs of Proper Deployment
Before device release, always check the five signs of proper Amulet™ deployment:
Compression on the lobe
Separation between the device lobe and disc
Concave disc
Axis of device lobe in line with axis of the LAA neck
Two-thirds device lobe distal to the left circumflex artery
If device position is unsatisfactory, recapture the device and redeploy per the IFU.
Notes: As with the AMPLATZER™ Cardiac Plug, there are five signs used to assess whether the Amulet™ device has been deployed appropriately. These should be evaluated prior to the device release.
The device lobe should show good compression.
There should be separation between the lobe and disc
The disc should be concave to show that the device is under tension
The axis of the device lobe should be parallel with the axis of the left atrial appendage neck
On echocardiography, the device lobe should be at least two thirds distal to the circumflex artery
If the device position is unsatisfactory, the device should be recaptured and redeployed.

## Slide 12
From: OAC Therapy Prescription in Patients With AF Across the Spectrum of Stroke Risk: Insights From the NCDR PINNACLE Registry
JAMA Cardiol. 2016;1(1):55-62
In this 429 417 patients US registry <50% of patients are treated according to the Guidelines!
Real World OAC for AF – PINNACLE Registry

## Slide 13
Tzikas A et al, EuroIntervention. 2016 Feb 20;11(10):1170-9
Multicentre experience with the AMPLATZER Cardiac Plug

## Slide 14
DESIGN: Non-randomized, single-arm, multi-center clinical evaluation of the ACP for stroke prevention in non-rheumatic AF patients
OBJECTIVE: To evaluate the acute and long-term safety and effectiveness of the ACP in clinical practice
PRINCIPAL INVESTIGATOR Apostolos Tzikas, Greece
Tzikas 2015
Study Flow Chart
Notes: 14
This is the Bulleted List slide.
To create this particular slide, click the NEW SLIDE button on your toolbar and choose the BULLETED LIST format. (Top row, second from left)
The Sub-Heading and footnote will not appear when you insert a new slide. If you need either one, copy and paste it from the sample slide.
If you choose not to use a Sub-Heading, let us know when you hand in your presentation for clean-up and we’ll adjust where the bullets begin on your master page.
Also, be sure to insert the presentation title onto the BULLETED LIST MASTER as follows:
Choose View / Master / Slide Master from your menu.
Select the text at the bottom of the slide and type in a short version of your presentation title.
Click the SLIDE VIEW button in the lower left hand part of your screen to return to the slide show. (Small white rectangle)

## Slide 15
Chart: 
| Risk of falls | Labile INR | Renal or hepatic disease | Previous minor bleeding | Stroke on warfarin | Drug interaction | CAD and stenting | High bleeding risk | Previous major bleeding
Indications for LAAO2 | 0.08 | 0.09 | 0.14 | 0.15 | 0.16 | 0.17 | 0.22 | 0.35 | 0.47
N=1047
Composite of previous bleeding (major or minor) and high bleeding risk = 73%
Indications for LAAO
Notes: 15
This is the Bulleted List slide.
To create this particular slide, click the NEW SLIDE button on your toolbar and choose the BULLETED LIST format. (Top row, second from left)
The Sub-Heading and footnote will not appear when you insert a new slide. If you need either one, copy and paste it from the sample slide.
If you choose not to use a Sub-Heading, let us know when you hand in your presentation for clean-up and we’ll adjust where the bullets begin on your master page.
Also, be sure to insert the presentation title onto the BULLETED LIST MASTER as follows:
Choose View / Master / Slide Master from your menu.
Select the text at the bottom of the slide and type in a short version of your presentation title.
Click the SLIDE VIEW button in the lower left hand part of your screen to return to the slide show. (Small white rectangle)

## Slide 16
Tzikas A et al, EuroIntervention. 2016 Feb 20;11(10):1170-9
Multicentre experience with the AMPLATZER Cardiac Plug

## Slide 17
Chart: Effectiveness in Annual Stroke Risk Reduction vs Estimated
| IC Bleeding | Other | Total
Reference | 0.058 | 0.056 | 0.056
Observed | 0.014 | 0.025 | 0.023
 | Patients | Total Patient Years | CHA2DS2-VASc Score
IC Bleeding | 188 | 287 | 4.5
Other | 813 | 1062 | 4.4
Total | 1001 | 1349 | 4.4
 | Estimated Annual Stroke Rate per CHA2DS2-VASc | Observed Annual Stroke Rate (N strokes + TIA)
IC Bleeding | 5.8% | 1.4% (4)
Other | 5.6% | 2.5% (27)
Total | 5.6% | 2.3% (31)
-75%
-55%
-59%
 | Patients | Total Patient Years | HAS-BLED Score
IC Bleeding | 188 | 287 | 3.5
Other | 813 | 1062 | 3.1
Total | 1001 | 1349 | 3.1
 | Estimated Annual Bleeding Rate per HAS-BLED | Observed Annual Bleeding Rate (N Bleedings)
IC Bleeding | 6.4% | 0.7% (2)
Other | 5.1% | 2.4% (26)
Total | 5.7% | 2.1% (28)
Chart: Effectiveness in Annual Bleeding Risk Reduction vs Estimated
| IC Bleeding | Other | Total
Reference | 0.061 | 0.054 | 0.057
Observed | 0.004 | 0.024 | 0.021
-89%
-47%
-60%
Stroke & Bleeding Reduction – ICB patients
Notes: 17
This is the Bulleted List slide.
To create this particular slide, click the NEW SLIDE button on your toolbar and choose the BULLETED LIST format. (Top row, second from left)
The Sub-Heading and footnote will not appear when you insert a new slide. If you need either one, copy and paste it from the sample slide.
If you choose not to use a Sub-Heading, let us know when you hand in your presentation for clean-up and we’ll adjust where the bullets begin on your master page.
Also, be sure to insert the presentation title onto the BULLETED LIST MASTER as follows:
Choose View / Master / Slide Master from your menu.
Select the text at the bottom of the slide and type in a short version of your presentation title.
Click the SLIDE VIEW button in the lower left hand part of your screen to return to the slide show. (Small white rectangle)

## Slide 18: LAA occlusion vs. standard care in patients with AF and intracerebral hemorrhage A propensity score matched follow-up study
J-E Nielsen-Kudsk – EuroPCR 2016
LAAO in IC Bleeding patients
Endpoint and Results
  Primary composite endpoint of all-cause mortality, ischemic stroke and major bleeding
  LAAO: Lower risk of composite outcome (Relative Risk Reduction: 81%)
  LAAO: Lower risk of mortality (Relative Risk Reduction: 92%)
  LAAO: Reduced risk for Stroke and major bleeding (Stroke RR 65%, major bleeding: 61%)
LAAO is suggested to be of major clinical benefit in AF patients with prior ICH
AF + ICH
176
787
147
147
LAAO
Standard
Propensity Score Match*
STROKECLOSE
RCT

## Slide 19
Tzikas 2016
Int J Cardiol 2016
LAAO & Renal Disease
375 patients with Chronic Kidney Disease (GFR<60)
Similar procedural safety
Dramatic reduction in Stroke/TIA, persistent in all stages of CKD
Patients with end-stage CKD had overall lower survival but the same frequency of MAEs at FU

## Slide 20
Am J Card 2016
Tzikas 2016
LAAO in the Elderly
LAAO was associated with:
similar procedural success in patients aged <75 and ≥75 years
older patients had a higher incidence of cardiac tamponade
At follow-up:
stroke and major bleeding rates were similar among groups

## Slide 21: Stroke Severity after LAAO?
Am J Cardiol. 2016 (in press)
LAAO with ACP: 1001 patients
N of Strokes at FU: 0.8% per year
81% of Strokes were Non Disabling (mRS<3)

## Slide 22: Peri-device Leaks
344 post procedural TEEs
Independent adjudication (Cardialysis)
Device-associated thrombus 3.2%
Peri-device leaks
minimal (<1mm) 5.5%
mild (1-3mm) 5.8%
moderate (3-5mm) 0.6%
severe (>5mm) 0.6%
Incidence and clinical impact of device-associated thrombus and peri-device leak following left atrial appendage closure with the Amplatzer Cardiac Plug
Jacqueline Saw1, MD, Apostolos Tzikas2,3, MD, PhD, Samera Shakir4, MD, Sameer Gafoor5, MD, Heyder Omran6, MD, Jens Erik Nielsen-Kudsk7, MD, Joelle Kefer8, MD, Adel Aminian9, MD, Sergio Berti10, MD, Gennaro Santoro11, MD, Fabian Nietlispach12, MD, Aris Moschovitis4 , MD, Ignacio Cruz-Gonzalez13, MD, Francis Stammen14, MD, Tobias Tichelbäcker15, MD, Xavier Freixa16, MD, Reda Ibrahim17, MD, Wolfgang Schillinger15, MD, Bernhard Meier4, MD, Horst Sievert5, MD, Steffen Gloekler4, MD
JACC Int 2016 (in press)

## Slide 23: Thank You